## Slide 1: Canny Edge Detection Using an NVIDIA GPU and CUDA
Alex Wade
CAP6938 Final Project

## Slide 2: Introduction
GPU based implementation of A Computational Approach to Edge Detection by John Canny
Paper presents an accurate, localized edge detection method

## Slide 3: Purpose
Canny’s edge detection algorithm involves a large number of matrix and floating point operations
Edge detection used as the first step for many computer vision tasks
Speeding up edge detection will increase computer vision performance, beneficial in cases such as live video feed processing

## Slide 4: Algorithm Steps
Image smoothing
Gradient computation
Edge direction computation
Nonmaxmimum suppression
Hysteresis

## Slide 5: Image Smoothing
Reduces image noise that can lead to erroneous output
Performed by convolution of the input image with a Gaussian filter
2 | 4 | 5 | 4 | 2
4 | 9 | 12 | 9 | 4
5 | 12 | 15 | 12 | 5
4 | 9 | 12 | 9 | 4
2 | 4 | 5 | 4 | 2
1
―
159
σ=1.4

## Slide 6: Image Smoothing

## Slide 7: Gradient Computation
Determines intensity changes
High intensity changes indicate edges
Performed by convolution of smoothed image with masks to determine horizontal and vertical derivatives
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1
1 | 2 | 1
0 | 0 | 0
1 | 2 | 1
x
y

## Slide 8: Gradient Computation
Gradient magnitude determined by adding X and Y gradient images
= x + y

## Slide 9: Edge Direction Computation
Edge directions are determined from running a computation on the X and Y gradient images
Edge directions are then classified by their nearest 45° angle
x
Θx,y = tan-1 
y

## Slide 10: Edge Direction Computation
0 ° 90 °
45 ° 135 °

## Slide 11: Nonmaximum Suppression
Used to localize edges
Uses edge direction classifications and gradient intensity values
For each pixel, determine whether its intensity value is higher than both of its perpendicular neighbors
All pixels that are not local maxima have their intensity values set to 0

## Slide 12: Nonmaximum Suppression

## Slide 13: Hysteresis
Determines final edge pixels using a high and low threshold
Image is scanned for pixels with a gradient intensity higher than the high threshold
Pixels above the high threshold are added to the edge output
All of the neighbors of a newly added pixel are recursively scanned and added if they fall below the low threshold

## Slide 14: Hysteresis

## Slide 15: Implementation Status
Currently Implemented on GPU
  Image Smoothing
  Gradient Computation
To be Implemented (currently use CPU)
  Edge Direction Computation
  Nonmaximum Suppression
May be Implemented (currently use CPU)
  Hysteresis
Will not be Implemented (done by CPU)
  File I/O

## Slide 16: GPU Implementation Details
Convolution kernels are sent to device global memory only once at initialization
Input and intermediate matrices are currently sent round trip from host to device texture memory for each step
  Three round trips
Kernel functions use fixed 256x256 block size

## Slide 17: Improvements to be Made
Implement edge direction computation and nonmaximal suppression
Improve GPU performance
  Eliminate unnecessary round trips
  Evaluate GPU memory use and correct as needed
  Combine steps to reduce computation
  Experiment further with block size
Try to implement hysteresis
General code optimization

## Slide 18: Performance Evaluation
Host
  Intel Core 2 Quad
  2.66 GHz
  3.25 MB RAM
Device
  NVidia GeForce 8800 GT
  512 MB Video Memory

## Slide 19: Performance Evaluation
Verified correctness of CPU only and GPU based implementations
Collected performance metrics on 256x256, 412x512, 1024x1024, and 2048x2048 input images
  Image smoothing time
  Gradient computation time (including transfer to GPU and back)
  Overall time excluding file I/O operations

## Slide 20: Performance Results
Chart: Gaussian Smoothing Performance
| 256 | 512 | 1024 | 2048
GPU | 1 | 1 | 4 | 14
CPU | 8 | 34 | 137 | 549

## Slide 21: Performance Results
Chart: Gradient Computation Performance
| 256 | 512 | 1024 | 2048
GPU | 0.5 | 1 | 4 | 13
CPU | 11 | 34 | 207 | 818

## Slide 22: Performance Results
Chart: Overall Performance
| 256 | 512 | 1024 | 2048
GPU | 39 | 124 | 465 | 1930
CPU | 43 | 143 | 597 | 2394